## Slide 1: 0x302 – Reading Out Firmware
ECED4406 – Computer Security
Dr. Colin O’Flynn
Dalhousie University.

## Slide 2: Finding Firmware

## Slide 3: Firmware Locations on Board
Initial view: Firmware is either:
Programmed into “internal” memory.
  -> E.g., like Arduino and other devices you may have used where the microcontroller contains the code.
Programmed into “external” memory.
  -> E.g., like Raspberry Pi where the microSD card contains the firmware.

## Slide 4: Typical Boot Process
First Stage Bootloader
Boot ROM
Linux Bootloader
Processor Core
Main “SoC” Chip
Small flash chip
MicroSD card or eMMC (large Flash)

## Slide 5: Where to Look for Firmware?
Firmware may be included in multiple locations on the board.
You may need to “read” all of the devices to understand the true boot process.

## Slide 6: Internal Flash Read-Out
Devices may have internal flash. These devices will typically require some sort of programmer to read. This may be device-specific. It is often disabled.
1. This microcontroller in a smart lock requires a specific programmer.

## Slide 7: “JTAG” Port
JTAG = Joint Test Action Group
JTAG in “Boundary Scan” Mode has access to all I/O pins.
TDO = Test Data Out
TDI = Test Data In
TCLK = Test Clock
TMS = Test Mode Select

## Slide 8: JTAG as a Debugger

## Slide 9: JTAG as a Debugger
Normally some sort of software gives us “Debug Access”
  Maybe allows read/writing of memory
  Maybe allows single-stepping and similar
Often devices will “lock out” debug or JTAG for security
  All devices should do this in production for security, but sometimes they don’t

## Slide 10: Cortex-M “SWD” Pins
“Serial Wire Debug” is a protocol that effectively reduces the JTAG pins to only needed 2 pins:
Serial Wire Debug Input Output (SWDIO)
Serial Wire Debug Clock (SWCLK)
On smaller Arm Cortex-M devices this is very common. You’ll often not see the full-size JTAG header or test points, and only find these two test points.
Normally it also has nRESET (NRST) and sometimes “Serial Wire Output” (SWO), a special additional debug out.

## Slide 11: Typical Embedded (Arm) Read-Out Attempts
JTAG Tool (Segger J-Link)
Target
Adapter to SWD Pins

## Slide 12: SPI Flash Chip Read-out
Example of a SPI flash chip (2) (often looks like this or the SOIC-8 below, ‘3’)

## Slide 13: SPI Flash Chip
Typical SPI flash pinout
(Can vary – check your device)
This example is from W25Q64FV

## Slide 14: SPI = Serial Peripheral Interface
SPI has a controller (historically may be called the master) that drives communication. It talks to the slave (peripheral) device.
Clock (SCK/SCLK)
Data FROM controller (COPI/MOSI)
Data FROM peripheral (CIPO/MISO)
Clock is driven from controller.
Controller Out Peripheral In
Controller In Peripheral Out
Chip Select (CS/SS)
Enable pin driven from controller to the specific peripheral.
Controller
Peripheral
SCK
COPI
CIPO
CS

## Slide 15: DSPI / QSPI = Dual/Quad SPI
Devices may support a higher-data-rate mode.
These devices always support the basic commands, and then allow a “switch” to faster modes.
For our work we don’t (normally) use those modes, but if you are sniffing the protocol will need to understand them.

## Slide 16: Reading out SPI Flash Devices
From Trammell Hudson: https://trmm.net/SPI_flash/
Various tools you can use include:
Bus Pirate with Flashrom
  Many tutorials online, such as https://ivanorsolic.github.io/post/hardwarehacking1/
Tigard with Flashrom
  https://github.com/tigard-tools/tigard#spi
Raspberry Pi with Flashrom
  https://nsideattacklogic-tech.blogspot.com/2018/06/dumping-spi-flash-memory-of-embedded.html
Trammell Hudson’s tool (see link at left)
…also many others!

## Slide 17: eMMC Flash Chip vs SPI Chip
Embedded Multi-Media Card
e.g., EMMC04G-W627

## Slide 18: eMMC Read-Out via SD Card Carrier

## Slide 19: eMMC / SD Card Links
https://www.blackhat.com/docs/us-17/wednesday/us-17-Etemadieh-Hacking-Hardware-With-A-$10-SD-Card-Reader.pdf
https://www.youtube.com/watch?v=6ofPbclXuZQ

## Slide 20: Firmware Read Out – Next Steps
With firmware read out – do some basic sanity checks as discussed in previous lecture (binwalk, strings, etc).
Then we can go ahead with reverse engineering steps.