## Slide 1: 0x409 – Ghidra Setup for Embedded R.E.
ECED4406 – Computer Security
Dr. Colin O’Flynn
Dalhousie University.

## Slide 2: Importing a Binary to Ghidra
Four important setup details we typically need:
Find the processor module to load (“language”).
Find the address offset of the binary.
Setup address space in Ghidra.
  OPTIONAL: Setup peripheral file (SVD).
Understand the interrupt vectors.

## Slide 3: STEP 1: Processor Module
Binary Data
Decoded into Machine Code
Assembly Language Output

## Slide 4: Example #1: Smart Lock
EM3587

## Slide 5: Arm Cortex-M
Find datasheet for main processor  EM3587  Arm Cortex-M

## Slide 6: Example #2: Phillips Hue 2.0 Bridge
From FCC filing – no screwdriver needed!
QCA4531

## Slide 7: MIPS 24Kc
MIPS 24Kc

## Slide 8: Example #3
STM32F303RCT7

## Slide 9: Arm Cortex-M

## Slide 10: Result of Step 1
Some devices (such as Arm Cortex-M) have an easy choice here.
Some devices may have lots of variants – may need to investigate what the most likely requirement is.
Sometimes have to try a few and see if some make “more sense”.
But first…

## Slide 11: STEP 2: Base Address
Why is file loaded at 0x8000000?

## Slide 12: Base Address: Processor / Architecture
Note – FLASH Memory starting at 0x8000000

## Slide 13: Offset Due to Bootloader
Bootloader 32 KB
Application Flash
Update Firmware File
0x80000000
0x80007FFF
0x80008000
0x80080000
0x00000
0x78000

## Slide 14: What If Offset is Unknown?
You can often load with a default base address (0), and then look at the results to see where loads are coming from:
Load from memory space 0x8000000
Base Address (0)
NOTE: many references are relative which means they “shift” with your specified base address.

## Slide 15: Result of Step 2
Remember – needed because this is binary, but in some cases update files may still have an offset due to the bootloader.
This “offset” is just used to skip parts of the file. Not the same as base address!
Set my base address here, and optionally specify a name for it.

## Slide 16: Step 3: Address Space Setup
Basic: Not Setup
Basic: Setup

## Slide 17: Main Advantage: Working XREFs
These are locations in SRAM referenced by the code – maybe globals for example, so once we determine what is stored in a global we can more easily track it’s usage.

## Slide 19: Accessing Memory Map Window

## Slide 20: After Address Space Setup
After doing address space setup  Run auto analysis again.

## Slide 21: Using Peripheral Debug Files
Many vendors provide files to help with debugging devices.
These formats will vary with vendor, but for Arm they are known as System View Description (SVD) files.

## Slide 22: Finding SVD Files
Check vendor website:
  E.g https://www.st.com/en/microcontrollers-microprocessors/stm32f303rc.html#cad-resources
Check github:
  Good large repo at https://github.com/cmsis-svd/cmsis-svd/tree/main/data
  Search other repos where they may be checked in…

## Slide 23: Leveldown SVD Loader
https://leveldown.de/blog/svd-loader/

## Slide 24: Step 4: Interrupt Vectors

## Slide 25: Understanding Interrupt Vectors in Ghidra
For some processors (e.g., Cortex) some of the base vectors are known and will be nicely annotated as here.
Sometimes they are not well specified and you’ll need to label them.

## Slide 26: Changing Data Types
Right Click
Double-click to jump to code

## Slide 27: Interrupt Vectors in Other Processors
On many devices there is no vector table, but instead the vectors have limited code-space. Normally “jump” instructions are encoded here.

## Slide 28: TIP #1: Using interrupt vectors to identify binaries
Vectors normally have very specific structure.
Often many are unused which will jump to the same default interrupt handler.
This applies across most architectures, not just Cortex-M – this example is an 8051 interrupt vector.

## Slide 29: TIP #2: Use Interrupt Vectors to Identify Base Address
Stack is at 0x20003DD0:
-> SRAM must be in that location. We would guess 0x20000000 maybe?
ISRs range from 0x80008A43-0x8011EEB
-> FLASH must be in that location. We might guess starts around 0x80000000?

## Slide 30: Final Step: Running Auto-Analysis
If doing this setup, suggest to NOT run auto-analysis when first loaded.
Do all your memory space / SVD setup, then run auto-analysis: